## Slide 1: Underwater Glider Audio Recorder
Sponsor: Metron, Dr. John Gebbie
Team Members: Chelsea Throop
Trevor Conant
Phu Nguyen
Saida Akhter

## Slide 2: Concept
There is increased interest in using underwater gliders for marine mammal research and monitoring
NEAR-Lab Webb Slocum Glider has currently implemented an off the shelf recording device with two hydrophones
Our goal is to design additional software and hardware to improve the usability of the device

## Slide 3: Project Goals
To improve current commercial audio recording device
  Inexpensive device that includes a user interface
  Records broadband signals over 30 days with up to 4 days of acoustic data
  Includes hardware and software updates

## Slide 4: Hardware
Three major updates to hardware
  Addition of a multiplexor to interchange up to 4 SD cards
  Separate Microcontroller unit and Real Time Clock for complex scheduled recordings
  Button interface for hands-free schedule programming

## Slide 5: Hardware- MUX

## Slide 6: Hardware- MCU and RTC

## Slide 7: Hardware- Button interface
Must be able turn on and record with out manually pressing buttons
Requires connection to send electrical signals as if button sequence is being pressed

## Slide 8: Hardware – MicroSD Storage
2x Fairchild FSSD06 Multiplexer
Each MUX interfaces 2x micro SD cards each
4 micro SD cards total, 128GB combined total storage
Each MUX input shares DAT bus connections from DSP on TASCAM
  Each has an Output Enable pin, when set high inputs have high impedance, no need for additional multiplexing of input signals.
Maximum power consumption for entire MUX system <0.01 mA

## Slide 9: Software
Three major components of software
  Pre-Mission user interface
  In-Mission recording schedule control
  Post-Mission data analysis

## Slide 10: Software- Pre-Mission
User interface : command line or GUI
  Allow user to program the schedule by inputting:
    recording and stand-by interval
    sample rate
    delay for start
  Confirm the schedule if the inputs are “good”
  Estimate maximum operation time of the system
  Set the operation parameters for the system

## Slide 11: Software- In-Mission
Control the operation as per programed schedule
Manage the data storage
  Store data to SD card
  Switch to the next available SD card when existing card “full”
  Reset power of “mainboard” to direct the data to targeted SD card

## Slide 12: Software- Post- Mission
Display list of audio files
Allow user to playback the records
Display the spectrogram and plots for analysis

## Slide 13: Schedule