## Slide 1: Underwater Sea Glider Audio Recorder
Team Members: Chelsea Throop
Trevor Conant
Phu Nguyen
Saida Akhter

## Slide 2: Concept
NEAR-Lab Sea Glider currently implements off the shelf recording device
Currently uses two hydrophones to gather acoustic data for oceanographic research
Our goal is to design additional software and hardware to improve the usability of the device

## Slide 3: Improved Feature Goals
Must be able to interface with TASCAM
Ability to access multiple SD cards
  Capable of 4 days of continuous recording
Capable of complex user selectable recording schedule
Recordings must be downloadable to laptop
Time stamps must be synchronized between recording device and GUI on laptop
Must be able to modify sample rate
Must be able to hear and/or display recordings (spectrogram)

## Slide 4: Feature Goals (Cont.)
Reasonable power consumption (alkaline batteries)
  4 days of continuous recording
  30 days of sleep mode
  Must create battery harness
Must develop hardware brackets to mount device in glider
  This depends on space available in glider
Completed device must weigh less than 0.5 kg

## Slide 5: Hardware

## Slide 7: Hardware – MicroSD Storage
2x Fairchild FSSD06 Multiplexer
Each MUX interfaces 2x micro SD cards each
4 micro SD cards total, 128GB combined total storage
Each MUX input shares DAT bus connections from DSP on TASCAM
  Each has an Output Enable pin, when set high inputs have high impedance, no need for additional multiplexing of input signals.
Maximum power consumption for entire MUX system <0.01 mA

## Slide 8: Software
User interface - command line, better – GUI
  User’s input : recording and stand-by interval, sample rate, delay for start
  Response:
    Set-up configuration if the inputs are “good”
    Estimated maximum operation time of the system
    Ask for confirmation
  Output to the system the confirmed operation set-points
  Display the signal spectogram

## Slide 9: Software
System:
  Control the operation:
    As per programed schedule -Interrupt from RTC
    Manage the data storage
      Store data to SD card
      Reset power when SD card “full” for switching to the next available SD card
    Manage the interfere between programmed schedule (RTC interrupt) and storage process.

## Slide 10: Schedule