## Slide 1: Capstone Proposal: Underwater Glider Audio Recorder
Sponsor: Metron, Dr. John Gebbie
Team Members: Chelsea Throop
Trevor Conant
Phu Nguyen
Saida Akhter

## Slide 2: Concept
There is increased interest in using underwater gliders for marine mammal research and monitoring
NEAR-Lab Webb Slocum Glider has currently implemented an off the shelf recording device with two hydrophones
Our goal is to design additional software and hardware to improve the usability of the device

## Slide 3: Project Goals
To improve current commercial audio recording device
  Inexpensive device that includes a user interface
  Records broadband signals over 30 days with up to 4 days of acoustic data
  Includes hardware and software updates

## Slide 4: Hardware
Three major updates to hardware
  Addition of a multiplexor to
  interchange up to 4 SD cards
  Separate Microcontroller unit
  and Real Time Clock for complex
  scheduled recordings
  Button interface for hands-free schedule programming

## Slide 5: Hardware- Data Storage
DSP on TASCAM (current off the shelf device) supports SDHC carts with FAT32 file format
  32GB max on pre-formatted SDHC cards.
Multiple SD cards needed to meet storage requirements.
  Requires multiplexing data bus to multiple devices
2x Fairchild FSSD06 multiplexer
Each MUX interfaces 2x micro SD cards each
4 micro SD cards total, 128GB combined total storage
Maximum power consumption for entire MUX system is <0.01 mW

## Slide 6: Hardware- Button interface
Must be able turn on and record with out manually pressing buttons
Requires connection to send electrical signals as if button sequence is being pressed

## Slide 7: Hardware- RTC
A number of RTC (ISL12082, DS1307, PCF2127, M41T82/83, DS1337) was looked at before selecting one.
Any of these could be used but we picked PCF2127
Feasibility of communicating with the MCU
Power consumption
Temperature compensated
Operating range
I2C bus interface
Programmable watchdog timer with interrupt

## Slide 8: Hardware- MCU
Several MPU were studied - 8-bit PIC MCUs, ATmega328p, PIC24F16KA101. All these are extreme low power Microcontrollers.
Among them 8-bit PIC MCU looked most suitable.
128KB Flash, 4KB RAM, Onboard EEPROM,
I2C, SPI, UART, USB, Ethernet
Operation down to 1.8V, sleep current as low as 20nA
Special low power BOR, WDT, RTC
Programmable Switch Mode Controller
Industry’s most robust offering

## Slide 9: Hardware- Block Diagram

## Slide 10: Software
Three major components of software
  Pre-Mission user interface
  In-Mission recording schedule control
  Post-Mission data analysis

## Slide 11: Software- Pre-Mission
User interface : command line or GUI
  Allow user to program the schedule by inputting:
    recording and stand-by interval
    sample rate
    delay for start
  Confirm the schedule if the inputs are “good”
  Estimate maximum operation time of the system
  Set the operation parameters for the system

## Slide 12: Software- In-Mission
Control the operation as per programed schedule
Manage the data storage
  Store data to SD card
  Switch to the next available SD card when existing card “full”
  Reset power of “mainboard” to direct the data to targeted SD card

## Slide 13: Software- Post- Mission
Display list of audio files
Allow user to playback the records
Display the spectrogram and plots for analysis

## Slide 14: Schedule